## Slide 1
EG7030 · WEEK 4
Progress Update
Duty Cycle-Aware Battery Degradation Analytics
for Electric Vehicle Fleet Applications
Usha Rani V. · Student ID: u2965962 · MSc Electric Vehicle Engineering
University of East London · Supervisor: Dr. Abdulrahman Albar · 23 June 2026

## Slide 2
Week 4 — Agenda
01
Literature Review
5 key papers on battery
degradation, ML & EV fleet
02
Dataset Analysis
NASA · CALCE · Oxford
Common features & structure
03
NMC Chemistry
Selection rationale &
cross-dataset relevance
04
EV Fleet Data
Fleet DNA delivery trucks
& related literature

## Slide 3
Literature Review — 5 Key Papers
RSC Advances 2025
Beyond Drive Cycles: EV Battery Health in Diverse Environments & Conditions
Mulpuri, Sah & Kumar
NMC-811 · SPMe · Drive cycles · SEI growth · Lithium plating · Duty-cycle degradation
Advanced Science 2025
Capacity Estimation & Knee Point Prediction Using EIS via Machine Learning
Si, Matsuda et al.
NMC-811 · EIS · XGBoost · SHAP · Knee detection · RUL prediction
J. Energy Storage 2025
Descriptive Proximity Modeling for Accurate & Explainable SoC Estimation
Inan et al.
LightGBM · DBSCAN clustering · SHAP · R2 ~ 1.00 · RMSE = 0.13
Nature Energy 2019
Data-Driven Prediction of Battery Cycle Life Before Capacity Degradation
Severson, Attia et al. (Stanford/MIT)
124 LFP cells · Early-cycle ML · Benchmark framework for SoH prediction
J. Open Research Software 2021
Python Battery Mathematical Modelling (PyBaMM)
Sulzer, Marquis, Timms et al. (Oxford)
SPMe/DFN models · SEI/crack/plating submodels · Dissertation simulation tool
Papers 1-3 confirmed from uploaded PDFs. Papers 4-5 are foundational benchmark literature.

## Slide 4
PAPER 1 (Most Relevant) · RSC Advances, 15, 30980-31004 (2025) · Mulpuri, Sah & Kumar · DOI: 10.1039/d5ra04379d
Beyond Drive Cycles: EV Battery Health in Diverse Environments
Key Findings
NMC-811 LGM50 21700 cylindrical cell (5 Ah) studied under real-world conditions
SPMe electrochemical model applied across 3 Indian regional driving patterns
Urban stop-go driving (Pattern 1) produces fastest capacity fade
Degradation modes: SEI layer growth, lithium plating, particle cracking
High C-rate charging + elevated temperature = compounding stress factors
Drive cycle metrics quantified: Kinetic Intensity (KI), RPA, PKE
Relevance to This Dissertation
Directly validates duty cycle → degradation link (core thesis)
NMC-811 = chemistry selected for this study
SPMe model = planned for PyBaMM simulation stage
Drive cycle metrics (KI, RPA, PKE) feed into Fleet Severity Index (FSI)
Addresses lab-to-real-world gap between datasets and EV fleets

## Slide 5
Papers 2 & 3 — ML Methods for Battery Health Estimation
Advanced Science 2025
Capacity Estimation & Knee Point
Prediction via EIS + ML (SHAP)
Si, Matsuda et al. | DOI: 10.1002/advs.202502336
NMC-811 (LiNi0.8Mn0.1Co0.1O2) positive electrode battery
EIS (Electrochemical Impedance Spectroscopy) as ML input features
XGBoost achieves high capacity estimation accuracy
SHAP identifies dominant EIS frequency features driving capacity loss
Knee-point detection enables early Remaining Useful Life (RUL) warning
J. Energy Storage 2025
Explainable SoC Estimation via
LightGBM & DBSCAN Clustering
Inan et al. | DOI: 10.1016/j.est.2025.118150
DBSCAN clustering segments battery charging behaviour patterns
LightGBM trained on: voltage, current, capacity, energy, cycles, temp
R2 approximately 1.00 and RMSE of 0.13 for SoC estimation
SHAP explains feature importance at each degradation stage
Outperforms LSTM and SVM baselines under dynamic drive profiles

## Slide 6
Papers 4 & 5 — Foundational & Methodology Literature
Nature Energy 2019
Data-Driven Prediction of Battery Cycle Life Before Capacity Degradation
Severson, Attia, Jin et al. (Stanford / MIT / Toyota)
124 LFP battery cells cycled to end of life under controlled conditions
Early-cycle (cycles 1-100) discharge features predict total battery lifetime
Elastic Net + Random Forest = benchmark ML prediction framework
Error < 9.1% for lifetime prediction on unseen test cells
Relevance: Foundational benchmark — our study extends to NMC & real fleet duty cycles
J. Open Research Software 2021
Python Battery Mathematical Modelling (PyBaMM)
Sulzer, Marquis, Timms, Hasan et al. (Univ. of Oxford)
Open-source Python framework for electrochemical battery modelling
Implements SPMe, DFN (Doyle-Fuller-Newman) and reduced-order models
Built-in degradation submodels: SEI growth, particle cracking, Li-plating
Integrates with Python ML ecosystem (NumPy, Pandas, scikit-learn)
Relevance: Directly cited in dissertation brief — used in Stage 5 simulation & validation

## Slide 7
Dataset Overview — NASA · CALCE · Oxford
NASA PCoE
Cells: B0005, B0006, B0007, B0018
Chemistry: LCO (Lithium Cobalt Oxide)
Type: 18650 cylindrical cells
EOL: 30% capacity fade threshold
Includes EIS impedance measurements
Cycling: CC-CV charge; constant discharge
Features: V, I, T, Capacity, Impedance
CALCE
CS2 & CX2 series: LCO chemistry
A123 series: LFP chemistry
INR 18650-20R: NMC (Samsung 2.0 Ah)
Multi-chemistry dataset (LCO, LFP, NMC)
Dynamic profiles: DST, FUDS, US06
Storage degradation data included
Features: V, I, T, Capacity, Resistance
Oxford
Cell series: BMP, BMR, SPM families
Format: .csv and .mat (MATLAB) files
NMC-type pouch cells
High-fidelity discharge profiles
Controlled temperature aging tests
Electrochemical characterisation included
Features: V, I, T, Capacity, SoC, SoH

## Slide 8
Common Ground Across All Three Datasets
V I T
Core Measurements
All three datasets record voltage, current & temperature — core ML features needed for SoH and SoC modelling
C
Capacity Fade Tracking
Capacity per cycle is available in all datasets — the primary indicator of State of Health (SoH) for fleet replacement decisions
SoH
SoH/SoC Derivation
Standard SoH = Q_current / Q_nominal can be derived from all three. RUL is derivable using end-of-life thresholds
DYN
Dynamic Profiles
CALCE (DST/FUDS) and Oxford include dynamic cycling closer to real EV operation; NASA adds EIS impedance data
CC-CV
Controlled Protocols
All use CC-CV charging, enabling standardised capacity check-up tests for cross-dataset degradation comparison
NMC
NMC Representation
CALCE INR 18650-20R and Oxford pouch cells are NMC — enabling consistent single-chemistry analysis for this study

## Slide 9
Why NMC Chemistry? — Four Key Reasons
1
Dataset Availability
CALCE INR 18650-20R (Samsung, 2.0 Ah) is confirmed NMC. Oxford pouch cells are NMC-type. Two datasets with NMC data enable cross-validated, consistent analysis.
2
Literature Alignment
Papers D1 (Mulpuri et al.) and D2 (Si et al.) both use NMC-811 cells. Using the same chemistry allows direct benchmarking of our ML results against published findings.
3
EV Market Dominance
NMC powers Tesla Model 3 LR, BMW i4, VW ID.4, Hyundai Ioniq 5 and represents 45-60% of global EV sales. Highest energy density among commercially available chemistries (200-250 Wh/kg).
4
Degradation Richness for SHAP
NMC undergoes SEI growth, particle cracking, lithium plating, Loss of Lithium Inventory (LLI) and Loss of Active Material (LAM). Rich multi-mode degradation enables meaningful SHAP feature attribution.
Selected: NMC (CALCE INR 18650-20R + Oxford pouch cells) — enables consistent cross-dataset ML training and benchmarking

## Slide 10
EV Fleet Data — Delivery Truck Duty Cycles
Fleet DNA Dataset (NREL)
Source: US National Renewable Energy Laboratory (NREL)
File: data_for_fleet_dna_delivery_trucks.csv (local)
Real-world commercial delivery truck GPS + drive data
Contains: speed profiles, distance, idle time, trip segments
Enables duty cycle severity metrics: KI, RPA, PKE, C-rate
Stop-go urban pattern = highest degradation risk (per D1 paper)
Dataset-to-Fleet Connection
Fleet stop-go patterns match CALCE DST/FUDS dynamic profiles
Urban cycle stress validates Oxford pouch cell aging conditions
Related Literature — EV Fleet Battery Health
Mulpuri et al. 2025 (RSC Advances)
Urban stop-go duty cycle causes ~2x faster NMC-811 degradation vs. highway — directly applicable to delivery fleet management
Severson et al. 2019 (Nature Energy)
Early trip data (first 100 cycles) predicts battery EOL — enables proactive fleet battery replacement scheduling
UK Zero Emission Vehicle Mandate (2024)
80% ZEV sales target by 2030 — fleet operators urgently need duty-cycle-aware battery health management tools
Faraday Battery Challenge (UK Gov.)
Identifies fleet duty cycle characterisation as a critical gap in commercial EV battery management

## Slide 11
Research Methodology — 7-Stage Framework
1
Data
Collection
NASA CALCE
Oxford Fleet DNA
2
Feature
Extraction
KI RPA PKE
FSI C-rate
3
EDA &
Analysis
Correlation
SoH trends
4
ML Model
Training
RF XGBoost
LGBM LSTM
5
SHAP
Explain.
Feature attr.
Duty-cycle link
6
PyBaMM
Simulation
SPMe model
NMC-811 valid.
7
Fleet
FSI Index
Novel metric
Risk scoring
Completed
Upcoming
Current Stage: 2-3 — Literature Review Complete · Data Downloaded & Organised · EDA Starting
Phase Timeline: May-Jun (Literature + Data) · Jul (ML Models) · Aug (SHAP + PyBaMM) · Sep (FSI + Writing + Submission)

## Slide 12
Next Steps — Weeks 5 & 6
Week 5 (24-30 Jun)
Complete EDA on CALCE NMC + Oxford datasets
Extract duty cycle metrics from Fleet DNA CSV (KI, RPA, PKE)
Compute prototype FSI scores for delivery truck routes
Correlation analysis: cycle severity vs. capacity fade rate
Week 6 (1-7 Jul)
Train baseline ML models: Random Forest, XGBoost, LightGBM
Generate initial SHAP feature importance plots
Draft Chapter 2 (Literature Review) — target 3,500 words
Read 3 additional papers from reference list